ENV 404 “Hazardous Waste Management” Assignment Set #1 Solution. Mar 14, 2018.

- Cd(OH)2 	 Cd+2 + 2OH-

| OH- | 4x(OH-)2 | Solubility of Cadmium (mol/L) |
| --- | --- | --- |
| 1E-14 | 4E-28 | 1.3325E+13 |
| 1E-13 | 4E-26 | 1.3325E+11 |
| 1E-12 | 4E-24 | 1332500000 |
| 1E-11 | 4E-22 | 13325000 |
| 1E-10 | 4E-20 | 133250 |
| 0.000000001 | 4E-18 | 1332.5 |
| 0.00000001 | 4E-16 | 13.325 |
| 0.0000001 | 4E-14 | 0.13325 |
| 0.000001 | 4E-12 | 0.0013325 |
| 0.00001 | 4E-10 | 0.000013325 |
| 0.0001 | 0.00000004 | 1.3325E-07 |
| 0.001 | 0.000004 | 1.3325E-09 |
| 0.01 | 0.0004 | 1.3325E-11 |
| 0.1 | 0.04 | 1.3325E-13 |
| 1 | 4 | 1.3325E-15 |

The solubility graph (of Cd+2 provided below between pH 5 and 9). Solubility of cadmium (mol per liter) depends on pH as you can see from the graph. The bold value provided above is for pH=7.

Figure 1. Solubility of cadmium depending on pH

- The following chemicals have the given Henry’s constants. Convert this constant into the dimensionless one.

| Compound | H ((atm*m3)/mol) | RxT ((atm*m3)/mol) | H’ (dimensionless) |
| --- | --- | --- | --- |
| Benzene | 5.5x10-3 | 0.024185 | 0.2274 |
| Phenol | 1.01x10-2 | 0.024185 | 0.4176 |
| Ethyl benzene | 7.07x10-3 | 0.024185 | 0.2923 |
| Tetrachloroethylene | 1.25x10-2 | 0.024185 | 0.5168 |
| Ethylenedichromate | 7.96x10-4 | 0.024185 | 0.0329 |

Note: H is divided by the R*T value (which was provided above) for the temperature of 20 °C (293.15 K) to find dimensioneless Henry’s constant.

3. log Koc = (0.681logBCF) + 1.963                        and        log Koc = (-0.55logS) + 3.64   Since maximum solubility is known, find logKoc first to find BCF values. The step by step solution was provided below:

| Compound | S | log S | logKoc | BCF |
| --- | --- | --- | --- | --- |
| Ethylbenzene | 152 mg/L | 2.18184 | 2.43999 | 5.012 |
| Hexachloroethane | 42 mg/L | 1.62325 | 2.74721 | 14.18 |
| Pentachlorophenol | 14 mg/L | 1.14613 | 3.00963 | 34.43 |
| Thallium sulfate | 4880 mg/L | 3.68842 | 1.61137 | 3.283 |
| Vinyl chloride | 4270 mg/L | 3.63043 | 1.64324 | 2.948 |

S: solubility (mg/L) in water. BCF stands for bioconcentration factor (L/kg).

- One cubic meter container holds 50 grams of hydrogen. Determine the pressure in the system (temperature is 25 °C).

Hydrogen gas MW = 2 grams/mol. n=50/2 = 25 moles. Ideal gas law states that temperature, volume and number of moles are the determinants in the container. By using P*V = n*R*T (in this Formula P is pressure (Pascal); V is molar specific volume (m3/(g*mol)); R is molar ideal gas law constant (8.3144 Pa*m3/(g*mol) and T is absolute temperature (K)

P = (n*R*T)/V  = 0.04*(8.3144)*(298.15)/1 = 99.15 Pa = 0.00098 atm

- Estimate the diffusion coefficient of methyl phenyl sulfide in water (t=25 C).

C7H8S is the chemical formula of the compound.

Compute molal volume using LeBas method (D=5.06*10-7*T)/(μ*V0.6)

C: 7*14.8 = 103.6

H: 8*3.7 = 29.6

S: 1*25.6 = 25.6_________

Sum: 158.8 cm3/mol=V

D = (5.06*10-7*298.15)/(0.89*158.80.6) = 8.1*10-6 cm2/s

6. A + 3B         2C

1000 kg per hour rate. MWA=32 g and MWB = 2 g.

30% conversion of A.

A is the limiting substance because B (2 grams) is 75% by weight. Therefore, theoretically for A 1000*0.25=250 kg is converted (or 250000/32=7812.5 moles per hour). For B, it is 1000*0.75=750 kg is converted (or 750000/2 = 375000 moles per hour). 3B is 375000 moles per hour (but A is the limiting substance again). 30% conversion of A means, only 0.30*250 = 75 kg of A is converted.

Total matter used to form C:

(2343.75 moles A) + (3*2343.75 moles for B) = 9375 moles (total)

for 2C. C is 4687.5 moles per hour.

2343.75 A + 7031.25 B       9375 C

2343.75*32 + 7031.25*2 = 9375*x

x = 9.5 grams per mole. This is the molecular weight of C. Check it: 9.5 grams per mole (molecular weight of C) is between 2 grams per mole (for B) and 32 grams per mole (for A). In addition, the value is close to 2 (more B is used compared to A).